# E08-041

In this circuit, the bulb is lit.

| Peter adds a second identical bulb, like this. |  | Sally adds a second identical bulb, like this. |
| --- | --- | --- |

| In Peter’s circuit, both bulbs are lit. But they are much dimmer than in the original circuit. |  | In Sally’s circuit, both bulbs are lit, with the same brightness as in the original circuit. |
| --- | --- | --- |

Explain why the bulbs are brighter in Sally’s circuit than in Peter’s:

______________________________________________________________

______________________________________________________________

______________________________________________________________

______________________________________________________________

______________________________________________________________

______________________________________________________________