TAP 104- 3: Electrons in copper

These problems are intended to help you practice calculations with large numbers of conducting particles and small amounts of charge found in a variety of examples of electrical conduction.

Copper conducting

As a rough guide, copper wires can conduct about 10 A mm2 before overheating and there are approximately 1020 free electrons per mm3 in copper.

Find:

1.	The number of electrons per second required to carry a current of 10 A.

2.	The length of wire with cross section 1 mm2 containing this number of electrons.

3.	The average drift velocity of electrons in the wire.

4.	If the same wire carried a current of only 10 mA what would the drift velocity be, and how long would it take a typical electron to drift through 1 mm?

Answers

1.	6.25 × 1019 electrons s–1

2.	0.625 mm

3.	0.625 mm s–1

4.	6.25 mm s–1; 160 s

External references

This activity is taken from Advancing Physics Chapter 2, 60S