TAP 108- 2: Introductory questions on resistance

1.	Convert the following:

(a)	12 500 Ω to kΩ

(b)	0.025 kΩ to Ω

2.	A 240 V lamp draws a current of 0.50 A from the mains supply. What is the resistance of the lamp?

3.	What current flows through a 12 V lamp when its filament has a resistance of 100 ? Give your answer in amps and milliamps.

4.	A current of 4.0 mA flows through a fine piece of resistance wire when the potential difference across it is 8.0 V. What is the resistance of the wire?

5.	A 5000 V EHT supply is protected by a 5 mega-ohm (5 M) resistor in series with its positive terminal. What is the maximum current that can be drawn from this supply if its terminals are shorted? (Ignore its internal resistance)

Answers

1 	(a) 12.5 Ωk (b) 25 Ω

2.	480 Ω

3.	0.12 A or 120 mA

4.	2000  or 2.0 k

5.	0.001 A or 1.0 mA